## Slide 1: Advanced Dial Plan and Routing for Webex Calling
2 Nov 2022
Fred Mollenkopf, Technical Solutions Architect Johannes Krohn, Principal Technical Marketing Engineer CTG

## Slide 2
Webex Calling Multi-Tenant Dial Plan Foundations - Fred
Webex Calling Multi-Tenant Routing Overview - Hannes
Webex Calling Multi-Tenant Caller Identity - Hannes
Interworking between Webex Calling and Unified CM on Premises - Fred
  Special Case: Flat Extension Dialling
Interworking between Webex Calling and Dedicated Instance - Hannes
  Cloud Connected PSTN for Dedicated Instance
Closing
Agenda
Advanced Dial Plan and Routing for Webex Calling

## Slide 3: Webex Calling Multi-Tenant Dial Plan Foundations

## Slide 4
Extension dialing: 2-6 digits (default 4)
  Inter- and intra-site; inter-site requires unique extensions
ESN (Location routing prefix + user extension) using an optional location code: up to 7 digits
+E.164
  Telephone numbers defined in the Webex Calling system. Always resolvable by +E164 dialing
Country Dial Plans
  US, Canada, Puerto Rico:
    National: 10 digit dialing or 1+10 digit dialing
    7 digit dialing:
      Webex Calling will normalize to E.164 for external calls assuming NPA of originator
      Dial plans in phones not optimized for 7D dialing  timeout experienced when using off-hook dialing
      Avoid conflict between abbreviated inter-site dialing (enterprise numbers) and 7D when integrating with PBX via Local Gateway; no 7D enterprise numbers
  Other countries
    Various digit lengths based on published national numbering plan
Webex Calling Multi-Tenant Dial Plan Foundations
Webex Calling dialing habits

## Slide 5
Primary number has as a dedicated field for extension, along with the telephone number (+E164), and is an optional value if a telephone number is assigned
Extensions are assigned to a location and can be used to provide ease of dialing
Country specific dial plans have numbering that will take precedence over extension assignment, e.g. NANP - 411 cannot be an extension for a US assigned location
Extensions can overlap between different locations:
  Within location takes precedence
  Can dial remote location if non-overlap
  Cannot disable extension lookup inter-location (e.g UCM partition approach)
  On-premises may have caveats (Unknown routing with overlap)
Webex Calling Multi-Tenant Dial Plan Foundations
Extension Dialing
NY
6001
+12125556001
Charlie
Widgets, Inc.
Montreal
4002
Dave
LA
4002
+13105554002
Bob
4001
+13105554001
Alice

## Slide 6
Allow for additional dialing behaviors for calling between locations using an ESN (Location routing prefix + user extension)
If you have multiple locations with the same extension, users must dial a prefix when calling between locations.
Prefixes can be a length of 2-7 digits. Optional steering digit should be used for extension conflict avoidance.
Used to align to existing UCM internal dial plans, either DN or Translation pattern defined
Webex Calling Multi-Tenant Dial Plan Foundations
Understanding location routing prefixes
NY
6001
82026001
+12125556001
Charlie
Widgets, Inc.
Montreal
4002
82514002
+15145554002
Dave
LA
4002
82014002
+13105554002
Bob
4001
82014001
+13105554001
Alice
Location | Location Code
LA | 8201
NY | 8202
Montreal | 8251

## Slide 7
The PSTN patterns available for dialing is dictated by the country type assigned for that location.
When the locations is created, a pre-loaded country dial plan is used for all devices within the location. This dial plan is reviewed and maintained by Cisco and is based off the ITU numbering plans.
Co-exists with telephone numbers defined on WxC org. Routing will be dependent on:
  Webex Calling #s defined for this Organization - subscriber +E.164 will be matched and routed directly to the user.
  No on-net match, the PSTN Connection is used to route any matched calls for these patterns.
Webex Calling Multi-Tenant Dial Plan Foundations
Dial Plans by Country
  https://help.webex.com/en-us/article/757iyo/Dial-plans-by-country

## Slide 8
Goal: optimize dial plan handling in phones to minimize timeouts
Outbound dialing digit (for example 9)
  Per location
Internal steering digit for inter-site (for example 8)
  Different from PSTN
Uniform location code length (for example 4)
  Location code includes leading internal steering digit!
Uniform extension length (for example 4)
Uniform inter-site dialing: steering digit – location id – extension
  Example: 8-496-9764
Webex Calling Multi-Tenant Dial Plan Foundations
Enterprise best practices

## Slide 9: Local Gateway
Available in 110+ countries
Continue using your existing provider
Support remote branch offices
Manage phone numbers Control Hub
Available in over 65 countries
Select from multiple world-class Cisco-certified providers
Choose providers on a site-by-site basis
Manage numbers in Control Hub
Available in the U.S., Canada, Europe, Australia and New Zealand
Single offer through Cisco and our partners
Fully integrated and managed from Control Hub
Cisco Calling Plans
(Cisco PSTN)
Cloud Connected PSTN Providers
Webex Calling Multi-Tenant Dial Plan Foundations
Call Routing for PSTN
Access
Network
Peering
network
CCPP
PSTN 1
CCPP
PSTN 2
Local
Gateway
PSTN
Cisco Calling Plans

## Slide 10: Trunks
Represents a single SIP Trunk to an on-premises device. Device can be registration based (CUBE) or MTLS based (CUBE + Future 3rd party)
Must be assigned to a Location. If used for PSTN the Country dial plan is based on location address.
Can be included in one or more Route Groups or can be directly associated to a Dial Plan.
Dial plans allow you to route calls to on-premises destinations by use of trunks or route groups.
Specifies the routing choice (trunk or route group) for calls that match any of its dial patterns.
Dial pattern represents on-premises extensions; ESN/on-net numbers, +E.164 patterns, SIP URI domains.
Logical grouping of Trunks (max. 10) for scale and redundancy of connections to the premises
Does not “live” in a Location
Route groups
Dial Plans
Webex Calling Multi-Tenant Dial Plan Foundations
Call Routing for On-Premise PBX & PSTN
CA PBX Dial Plan
us.foo.com
8408XXXX
+1408525XXXX
8310XXXX
+1310444XXXX
US East (Route Group)
Local Gateway
Trunk

## Slide 11
Webex Calling Multi-Tenant Dial Plan Foundations
PSTN connection options
Enterprise
Trunk SJ
US West 1 Route Group
Trunk UK
US West 2 Route Group
Trunk LA
CCPP 1
CCPP 2
SJ CUBE
LA CUBE
UK CUBE
Location NY
#1
#1
Cisco PSTN or Cloud Connected PSTN
Premises-based PSTN (Local Gateway)
#1
#1
PSTN connection
Note: Cloud Connected PSTN Providers are only accessible to Webex Calling users or Dedicated Instance, not premises PBX users.
No routing from trunk to PSTN
Location RTP
PSTN connection
Location Dallas
PSTN connection
Location SJC
PSTN connection
Location LA
PSTN connection
Location London
PSTN connection
Location Glasgow
PSTN connection
#2

## Slide 12: Webex Calling Routing Overview

## Slide 13
Multiple phases
Source classification (PSTN, user, premises)
  Based on source only
  or in the case of trunks based on caller ID match on dial plan pattern
  or for extensions as caller ID based on extension length and unknown extension dialling policy
Destination selection
Screening & Routing (User, Trunk/Route Group, PSTN)
Webex Calling Multi-Tenant Routing Overview
Webex Calling call routing overview

## Slide 14
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Destination selection

## Slide 15
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
Destination selection
Yes
PSTN
2

## Slide 16
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
User
Destination selection
E.164, ext, ESN
Yes
PSTN
2
Yes
User
2
Test dialed number against +E.164, extension, and enterprise numbers of users within customer.
Exact match: “9011496100123” <> “+496100123”

## Slide 17
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
User
VON
Dial Plan
Destination selection
E.164, ext, ESN
Strict match
Yes
PSTN
2
Yes
User
2
Yes
VON
2
Yes
DP
2
RL
Yes
RL
2
Strict match
Strict match: ”914085550123“ does not match “+1408555!“

## Slide 18
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
User
VON
Dial Plan
NS lookup
PSTN
Unknown number
Destination selection
E.164, ext, ESN
Strict match
Yes
PSTN
2
Yes
User
2
Yes
VON
2
Yes
DP
2
2
Based on national dial plan
+E.164 translated
RL
Yes
RL
2
Strict match
Dialed number might be translated to +E.164 based on national numbering plan.
For example:
9011496100123  +496100123
If number is translated, then go back to check for internal matches

## Slide 19
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
User
VON
Dial Plan
NS lookup
PSTN
?
Unknown number
Yes
Unknown ext.
Destination selection
E.164, ext, ESN
Strict match
Unknown extension policy enabled and 2-6 dialed digits
Yes
PSTN
2
Yes
User
2
Yes
VON
2
Yes
DP
2
2
2
Unknown number handling
Based on national dial plan
+E.164 translated
RL
Yes
RL
2
Strict match

## Slide 20
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
User
VON
Dial Plan
NS lookup
PSTN
?
Unknown number
Location PSTN
Yes
Unknown ext.
prem PSTN
Destination selection
E.164, ext, ESN
Strict match
Unknown extension policy enabled and 2-6 dialed digits
Cloud PSTN
Yes
PSTN
2
Yes
User
2
Yes
VON
2
Yes
DP
2
2
2
Unknown number handling
Based on national dial plan
+E.164 translated
RL
Yes
RL
2
Strict match

## Slide 21
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
User
VON
Dial Plan
NS lookup
PSTN
?
Unknown number
Location PSTN
Yes
Unknown ext.
prem PSTN
Destination selection
Block or allow based on calling permissions and route
E.164, ext, ESN
Strict match
Unknown ext.
Legacy
Standard
Unknown Number
Unknown extension policy enabled and 2-6 dialed digits
Cloud PSTN
Yes
PSTN
2
Yes
User
2
Yes
VON
2
Yes
DP
2
2
2
2
Unknown number handling
Based on national dial plan
+E.164 translated
RL
Yes
RL
2
Strict match

## Slide 22
Webex Calling Multi-Tenant Routing Overview
Routing overview
User dials number
Emergency
User
VON
Dial Plan
NS lookup
PSTN
?
Unknown number
Location PSTN
Yes
Unknown ext.
prem PSTN
Destination selection
Block or allow based on calling permissions and route
E.164, ext, ESN
Strict match
Unknown ext.
Route to user
PSTN VON
Call Type
RL
DP unknown ext.
User
Legacy
Unknown Number
Unknown extension policy enabled and 2-6 dialed digits
Cloud PSTN
Yes
PSTN
2
Yes
User
2
Yes
VON
2
Yes
DP
2
2
2
2
2
Unknown number handling
Based on national dial plan
+E.164 translated
RL
Yes
RL
2
Route to Location PSTN
Strict match
Meeting number
Route to meetings SRV for location’s country
Route to Trunk/RG
Based on dial-in numbers table
Yes
No
Standard

## Slide 23
Webex Calling Multi-Tenant Routing Overview
Unknown* Number Incoming Call Handling
Calling Device/Number |  | Unknown Numbers Handling for Premises-based PSTN: | 
Device | Number | “Standard behavior” | “Legacy behavior”
Trunk | Unknown Extension (2-6 digits, e.g., 4099) | Premises | Premises
 |  | External | 
 | Other Unknown Number (e.g., 72349999) | External | Premises
enabled
disabled
“Enable routing unknown extensions to the Premises as internal calls” (location setting):
*unknown: caller id does not match any dial plan pattern or route list

## Slide 24
Webex Calling Multi-Tenant Routing Overview
Unknown* Number Incoming Call Handling
Calling Device/Number |  | Unknown Numbers Handling for Premises-based PSTN: | 
Device | Number | “Standard behavior” | “Legacy behavior”
Trunk | Unknown Extension (2-6 digits, e.g., 4099) | Premises | Premises
 |  | External | 
 | Other Unknown Number (e.g., 72349999) | External | Premises
Basically: call from any unknown number treated as premises call
enabled
disabled
“Enable routing unknown extensions to the Premises as internal calls” (location setting):
*unknown: caller id does not match any dial plan pattern or route list

## Slide 25
Webex Calling Multi-Tenant Routing Overview
Unknown* Number Incoming Call Handling
Calling Device/Number |  | Unknown Numbers Handling for Premises-based PSTN: | 
Device | Number | “Standard behavior” | “Legacy behavior”
Trunk | Unknown Extension (2-6 digits, e.g., 4099) | Premises | Premises
 |  | External | 
 | Other Unknown Number (e.g., 72349999) | External | Premises
enabled
disabled
“Enable routing unknown extensions to the Premises as internal calls” (location setting):
Classification of calls from extensions depends on location level setting for unknown extension dialing
*unknown: caller id does not match any dial plan pattern or route list

## Slide 26
Webex Calling Multi-Tenant Routing Overview
Unknown* Number Incoming Call Handling
Calling Device/Number |  | Unknown Numbers Handling for Premises-based PSTN: | 
Device | Number | “Standard behavior” | “Legacy behavior”
Trunk | Unknown Extension (2-6 digits, e.g., 4099) | Premises | Premises
 |  | External | 
 | Other Unknown Number (e.g., 72349999) | External | Premises
enabled
disabled
“Enable routing unknown extensions to the Premises as internal calls” (location setting):
Classification of calls from extensions depends on location level setting for unknown extension dialing
Note: “Enable routing unknown extensions to the Premises as internal calls” setting does not only affect routing of calls TO the premises but also treatment of calls FROM the premises
*unknown: caller id does not match any dial plan pattern or route list

## Slide 27
Webex Calling Multi-Tenant Routing Overview
Unknown Number Outgoing Call Handling
Call Types and Destinations |  | Unknown Numbers Handling for Premises-based PSTN: | 
From | To | “Standard behavior” | “Legacy behavior”
WxC | Unknown Extension (e.g., 4099) | Route to Premises | 
 |  | Block | Route to External
WxC | Other Unknown Number (e.g., 72359999) | Block | Route to External
Premises | Unknown Extension (e.g., 4099) | Route to Premises | 
 |  | Block | 
Premises | Other Unknown Number (e.g., 72359999) | Block | 
External | Any Unknown Number (e.g., 4099, 72359999) | Block | 
enabled
disabled
“Enable routing unknown extensions to the Premises as internal calls” (location setting):

## Slide 28
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)

## Slide 29
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)
Calls from Webex Calling users can be routed everywhere

## Slide 30
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)
Calls from DI users can be routed everywhere

## Slide 31
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)
Call from premises classified as user call: no access to cloud PSTN (in contrast to call from DI user)

## Slide 32
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)
Call from premises classified as PSTN call: no access to cloud PSTN nor other trunks; premises PSTN can only be used for premises users, DI users, and Webex Calling users, but not for premises users in other sites

## Slide 33
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)
Cloud PSTN can only be used for Webex Calling users and DI users, but not for premises users

## Slide 34
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
No tandem between premises (user and PSTN) and Cloud PSTN
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)

## Slide 35
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
  On-premises users behind trunks cannot use Cloud PSTN, DI users can
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)

## Slide 36
Webex Calling Multi-Tenant Routing Overview
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
  Trunk to trunk not allowed for calls from premises PSTN
*prem user vs PSTN: caller ID match on DP pattern, or extension (see prev. slides)

## Slide 37: Webex Calling Multi-Tenant Caller Identity

## Slide 38
Webex Calling Multi-Tenant Routing Overview
Incoming Call Handling Logic – Caller ID and Call Type
* : It is possible to decide whether to present both or only the “From:” when the call is routed to a trunk
Calling Device/Number |  | Call Type | WxC Caller Identity
WxC endpoint |  | WxC | Internal caller identity in profile
Trunk | Caller ID: RL match | WxC | Identity in “From:” header
 | Caller ID: DP match | Premises | Identity in “From:” header
 | Caller ID: no match | External | Identity in “From:” header
Cloud PSTN (CCP, SP PSTN, Cisco PSTN…) |  | External | Keep both “From:” and PAI header information *

## Slide 39
Webex Calling Multi-Tenant Routing Overview
Outgoing Caller ID
Call Types and Destinations |  | Outgoing Routing Behavior | Outgoing Caller Identity | 
From | To |  |  | 
WxC | WxC endpoint | Route to WxC | Internal caller identity in profile | 
 | Route List or Dial plan | Route to Premises | E.164 | (based on “Caller ID format for calls from and to premises”)
 |  |  | ESN | 
 | PSTN | Route to External | External caller identity in profile | 
Premises | WxC endpoint | Route to WxC | Incoming “From:” | 
 | Route List or Dial Plan | Route to Premises | Incoming “From:” | 
 | PSTN | Block | N/A | 
External | WxC endpoint | Route to WxC | Incoming “From:” | 
 | Route List | Route to Premises | Incoming “From:” | 
 | Dial plan | Block | N/A | 
 | PSTN | Block | N/A | 

## Slide 40
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 

## Slide 41
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 
PAI always has TN as +E.164. Only exception: if user has no TN then the main number of the user’s location is used

## Slide 42
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 
“Caller ID Format for Calls from and to On-premises” only affects From header

## Slide 43
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 
If +E.164 is desired and the user has a TN Webex Calling uses the TN

## Slide 44
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 
If +E.164 is desired and the user has no TN then the caller ID is determined by the user’s caller ID setting

## Slide 45
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 
If ESN is desired and the user has an extension then ESN (location prefix + extension) is used. W/o location prefix configured extension.

## Slide 46
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 
If ESN is desired and the user has no extension then user’s +E.164 caller id is used as fallback

## Slide 47
Webex Calling Multi-Tenant Caller Identity
Caller ID for Calls from Webex Calling to Trunks
TN and/or extension configured? |  |  | “Caller ID Format for Calls from and to On-premises” | 
 |  |  | +E.164 | ESN
TN | Extension | PAI | From | From
Yes | Yes | TN, +E.164 | TN, +E.164 | Location prefix + extension
Yes | No | TN, +E.164 | TN, +E.164 | According to user caller ID configuration, +E.164
No | Yes | Location main number, +E.164 | According to user caller ID configuration, +E.164 | Location prefix + extension
No | No | No calls allowed without either TN or extension configured |  | 
We can have different caller ID formats in From: and PAI:. This can be useful when using premises PSTN and still requiring extension dialling between Webex Calling and premises users.

## Slide 48: Interworking between Webex Calling and Unified CM On-Premise

## Slide 49
Interworking between Webex Calling and Unified CM On-Premise
Webex Calling service settings for premises call routing
Standard: Calls treated as premises or external based on caller id – requires dial plan
Legacy: unknown calls treated as premises
Choose caller ID format for calls from Webex Calling to PBX

## Slide 50
Outgoing calls:
Processes on defined pattern matching
Allows for unknown matching on extensions
Control Hub text doesn’t reflect order of operation
Incoming calls:
Caller ID matching is enforced to determine external or premise calls
Required match for specific call routing transit scenarios (e.g. Trunk to Trunk calls)
Provides support for internal versus external feature use (e.g. Executive Filter on internal vs. external)
Interworking between Webex Calling and Unified CM On-Premise
Standard behavior for unknown number handling
This is the default and recommended option to achieve the best level of interoperability with an on-premises PBX

## Slide 51
Interworking between Webex Calling and Unified CM On-Premise
Call flows From WxC to UCM
Internet
Site 3
Enterprise A
Site 1
LGW
Cisco Calling Plan
CCPP
PSTN
Site 2
WxC user dials +E.164* of UCM user
80011001
+13105551001
GW
UCM
80011002
Non-DID
2001
80022001
+12125552001
3001
80033001
+14085553001
* Webex Calling will normalize country national or international numbers into +E.164 during routing analysis
80011002 dialed
WxC user dials ESN of UCM user
WxC user dials a Non-E.164 PSTN number
+13105551001 dialed
411 dialed

## Slide 52
How a call is matched during outbound routing can affect how the call is presented to UCM
Dial Plan match
  Will be checked on initial route lookup or on a re-tried +E.164 lookup
  Routes as Premise Call
  Caller ID will be based on Service Settings value
NS lookup based on the country dial plan
  Country is determined by the calling source’s location
  Routes as PSTN External Call
  Caller ID will be based on External Caller ID
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM – Outbound routing check
Dial Plan
NS lookup
PSTN
Yes
DP
2
2
Based on national dial plan
Strict match

## Slide 53
Dial Plan is created with +E.164 numbers or pattern ranges residing on Unified CM
  Dial Plans are global for an Enterprise and apply to all their users regardless of Location
   Routing choice for given Dial Pattern is same for everybody
ESN used for ITN dial plans
Can use multiple LGWs for scale and redundancy
Avoidances:
  Extensions – can cause issues in country dial plans for global deployments and unscalable for overlap ranges
  TEHO – forces all locations dialing that pattern to egress through a single point, not supported by TAC
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM - Dial plan outgoing match +E.164 & ESN
SJ Trunk A
CA-RG-1 Route Group
LA Trunk A
SJ CUBE
LA CUBE
#1
#2
CA PBX Dial Plan
us.foo.com
8408XXXX
+1408525XXXX
8310XXXX
+1310444XXXX

## Slide 54
Dial Plan is created with +E.164 numbers or pattern ranges residing on Unified CM
  Dial Plans are global for an Enterprise and apply to all their users regardless of Location
   Routing choice for given Dial Pattern is same for everybody
ESN used for ITN dial plans
Can use multiple LGWs for scale and redundancy
Avoidances:
  Extensions – can cause issues in country dial plans for global deployments and unscalable for overlap ranges
  TEHO – forces all locations dialing that pattern to egress through a single point, not supported by TAC
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM - Dial plan outgoing match +E.164 & ESN
SJ Trunk A
CA-RG-1 Route Group
LA Trunk A
SJ CUBE
LA CUBE
#1
#2
CA PBX Dial Plan
us.foo.com
8408XXXX
+1408525XXXX
8310XXXX
+1310444XXXX
Extensions: extension routing to premises is established by using the unknown extension routing policy on a Webex Calling location
TEHO: Webex Calling dial plans are meant to establish routes to premises (not PSTN!) destinations. Calls from PSTN will be wrongly classified as premises calls.

## Slide 55
numeric_pattern := ("+" 1*DIGIT [( "!" / 1*"X" )]) / (1*DIGIT [ 1*"X" ])
  Where DIGIT := “0“ - “9“
Wildcards:
  X : represents a single digit (0-9)
  ! : represents a sequence of one or more digits (0-9); only allowed with +E.164 prefixes
Examples:
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM - Numeric dial pattern syntax
+1408555XXXX | 11-digit +E.164 number starting with +14085555
+14085551234 | exact dial string +14085551234
+496100! | any dial string starting with +496100
84969XXX | 8-digit ESN starting with 84969
84969764 | exact 8-digit ESN 84969764

## Slide 56
The outbound dial string is analyzed based on the national dial plan of the calling user
National dials plans will try to globalize to +E.164 for routing if possible (Toll-Free, National and International)
Non-E.164 patterns are not adjusted
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM – National dial plan outgoing match
  US NANP 10-digit example
  A 10-digit pattern will match and prepend the plus and the country code

## Slide 57
The outbound dial string is analyzed based on the national dial plan of the calling user
National dials plans will try to globalize to +E.164 for routing if possible (Toll-Free, National and International)
Non-E.164 patterns are not adjusted
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM – National dial plan outgoing match
  US NANP 7-digit example
  A 7-digit pattern will match and prepend plus, country code and NPA
  The source caller’s NPA is used to fill in the blanks!
  Digits sent to LGW will be full +E164
  US NANP 10-digit example
  A 10-digit pattern will match and prepend the plus and the country code

## Slide 58
The outbound dial string is analyzed based on the national dial plan of the calling user
National dials plans will try to globalize to +E.164 for routing if possible (Toll-Free, National and International)
Non-E.164 patterns are not adjusted
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM – National dial plan outgoing match
  US NANP 7-digit example
  A 7-digit pattern will match and prepend plus, country code and NPA
  The source caller’s NPA is used to fill in the blanks!
  Digits sent to LGW will be full +E164
  US NANP 10-digit example
  A 10-digit pattern will match and prepend the plus and the country code
  US special numbers example
  A 3-digit number will be delivered as dialed
  Non-E164 will require pattern routing on UCM

## Slide 59
Unified CM needs to support ESN and +E.164 as called address for calls from WxC
+E.164
  trivial, match on +E.164 DN or PSTN RP
ESN
  match on ESN dialing normalization pattern in OnNetRemote partition
  Called party gets normalized to +E.164
  calling search space inheritance on TP: same calling search space used again for post-translation lookup
  Match on +E.164 DN
Non-Preferred Architecture designs, apply appropriate translations before DN lookup!
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM – Incoming to UCM +E.164 & ESN Matches
DN
All IP Phone DNs (+E.164)
CSSs
Partitions
Trunk Inbound CSS
Webex Calling LGW
Trunk
81012.XXX, Pre-Dot, Prefix +12125550
OnNetRemote
\+1XXXXXXXXXX \+!
PSTN
LRG / RL / GW

## Slide 60
PSTN calls from WxC use the PSTN native national number format for Non-E.164
Non-E.164 numbers
  RP must include special numbers
  Redundancy is handled by UCM Route lists
This enforces a country boundary on the Trunk between UCM and WxC due to Non-E.164 potential overlap
  Solution – Duplicate end-to-end trunk configuration to route for multi-country Non-E.164
  This can be achieved with a single CUBE in centralized trunking scenarios using multiple tenants on the CUBE.
Interworking between Webex Calling and Unified CM On-Premise
WxC to UCM – Incoming to UCM PSTN specific matches
DN
All IP Phone DNs (+E.164)
CSSs
Partitions
US Trunk
Inbound CSS
Webex Calling LGW
Trunk
81012.XXX, Pre-Dot, Prefix +12125550
OnNetRemote
\+1XXXXXXXXXX \+!
411
US PSTN
LRG / RL / GW

## Slide 61
Interworking between Webex Calling and Unified CM On-Premise
Call flows From UCM to WxC
Internet
Site 3
Enterprise A
Site 1
LGW
Cisco Calling Plan
CCPP
PSTN
Site 2
UCM user dials +E.164 of WxC user
80011001
+13105551001
GW
UCM
80011002
Non-DID
2001
80022001
+12125552001
3001
80033001
+14085553001
+12125552001 dialed
80011002 dialed
UCM user dials ESN of WxC user
PSTN caller dials +E.164 of WxC User
+14085553001 dialed

## Slide 62
With a single Egress LGW selection not site specific  no LRG based LGW selection required*
Multiple LGWs in multiple locations: RL and LRG
Can can use multiple LGWs for scale and redundancy
Webex Calling destinations provisioned as +E.164 route patterns
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC - +E.164 Outbound Route Patterns
DN
All IP Phone DNs (+E.164)
CSSs
Partitions
NYCInternational
1XX, Prefix +12125550
9.[2-9]XXXXXX, Pre-Dot, Prefix +1212
NYCtoE164
+E.164 RPs for all Webex Calling destinations
WebexCalling
Remaining Partitions
Webex Calling RL
Webex Calling RG
Route Lists
Route Groups
*For extension dialling w/ non-unique extensions site specific trunks are required so that Webex Calling can establish proper dialling context. LRG can be used for site specific egress trunk selection

## Slide 63
Any dialing habit can be transformed to +E.164 using dialing normalization translations
Dialing normalization for Webex Calling ESN ranges to +E.164 in same partition as Webex Calling route patterns
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC – ESN Outbound Route Patterns
DN
All IP Phone DNs (+E.164)
CSSs
Partitions
NYCInternational
DN
1XX, Prefix +12125550
9.[2-9]XXXXXX, Pre-Dot, Prefix +1212
NYCtoE164
\+140855501XX
WebexCalling
Webex Calling RL
Webex Calling RG
Route Lists
Route Groups
81012.XXX, Pre-Dot, Prefix +12125550
OnNetRemote
81101.1XX, Pre-Dot, Prefix +14085550

## Slide 64
Any dialing habit can be transformed to +E.164 using dialing normalization translations
Dialing normalization for Webex Calling ESN ranges to +E.164 in same partition as Webex Calling route patterns
Better solution: use ESN route patterns for Webex Calling ESN ranges  also works with extension only Webex Calling destinations
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC – ESN Outbound Route Patterns
DN
All IP Phone DNs (+E.164)
CSSs
Partitions
NYCInternational
DN
1XX, Prefix +12125550
9.[2-9]XXXXXX, Pre-Dot, Prefix +1212
NYCtoE164
\+140855501XX
WebexCalling
Webex Calling RL
Webex Calling RG
Route Lists
Route Groups
81012.XXX, Pre-Dot, Prefix +12125550
OnNetRemote
81101.1XX

## Slide 65
PSTN Dial Plan can utilize the same Route Patterns for +E.164 dialing as UCM users.
If PSTN gateway is sending only a subset of digits to UCM, the number will need to be converted to +E.164 before sending to WxC.
Multiple ways to do on UCM:
  Called Party Transformation Patterns (preferred)
  Translation Pattern (shown)
  Route Patterns
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC – PSTN Outbound Route Patterns
DN
All IP Phone DNs (+E.164)
CSSs
Partitions
Trunk Inbound CSS
PSTN Gateway
Trunk
+E.164 RPs for all Webex Calling destinations
WebexCalling
Webex Calling RL
Webex Calling RG
Gateway Translations
1XXX, Prefix +1408555

## Slide 66
Best practice on Unified CM: “globalize on ingress, localize on egress”*
Calling party transformation
  Side-effect of routing: calling party transform on RP/TP
  Explicit: calling party transformation patterns, calling party transformation CSS on SIP trunk
If global DN format is used on Unified CM then no Webex Calling specific upstream calling party transformation is required
  Both, +E.164 or ESN are acceptable caller ID formats
For other formats caller ID needs to be transformed to +E.164 (preferred) or ESN (fallback for non-DID users).
PSTN format can be delivered in National or +E.164 (preferred) format.
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC - Caller ID for Calls
*see “Preferred Architecture for Cisco Collaboration 14 Enterprise On-Premises Deployments, CVD”

## Slide 67
Different Number formats commonly used in calling deployments
Calling party is key for proper call classfication (prem vs. PSTN)
  Dial plan match for number formats with global significance (ESN, +E.164)
  Number length and unknown extension policy enabled for extensions
Prem classification important for: extension/ESN dialling, trunk-to-trunk calls, calling features with differentiated treatment for prem vs. PSTN calls
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC - Enterprise Number Formats for Calls
 | Example | Calling Party Requirements | Called Party
Extension | 1501 | 2-6 digits, unknown extension policy enabled on trunk‘s location | Call routed in context of pilot user of trunk’s location
ESN | 8 496 9764 | Dial plan match | Unique address
+E.164 | +1 408 555 0123 | Dial plan match | Unique address

## Slide 68
Inbound to Webex Calling, the originating trunk is identified by the otg tag inserted into the “From” header by the Local Gateway
Call classification checks the unscreened caller ID and is matched against dial plan patterns
  If a match is found, then the call is classified as premises call
  If no match is found, then the call is classified as external call
Before routing to the called destination, call classification determines which destinations can be reached via transit routing:
  Premise calls - allowed transit routing is WxC Org number or Trunks
  External calls - will restrict the call to WxC Org numbers only
  CCPP or Cisco PSTN are not supported via transit routing
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC – Inbound E.164 & ESN matching
SJ Trunk A
SJ CUBE
otg=sj-lgw
Calling Party Number
+14085251000
CA PBX Dial Plan
us.foo.com
8408XXXX
+1408525XXXX
8310XXXX
+1310444XXXX
Premise Call
Transit Routing
WxC Org Numbers
Trunks
CCPP
Cisco PSTN

## Slide 69
Interworking between Webex Calling and Unified CM On-Premise
UCM to WxC - PSTN Number Format Considerations
Calling
Site 1
Local GW
Site 2
Internet
CCPP
Cisco Calling Plan
PSTN
Caller ID from PSTN | Called Party number Format | Call routing with Standard Behavior
+E.164 or National | +E.164 | 
+E.164 or National | E.164 (NANP 11D) | 
+E.164 or National | National (NANP 10D) | 
+E.164 or National | Extension | (extension dialling only possible for prem calls)
Note: Caller ID sent to Webex Calling must be in the format of a supported dialling habit. Keep in mind that it might end up in a missed calls directory…

## Slide 70: Special Case: Flat Extension Dialing

## Slide 71
Non-overlapping extension ranges in all locations
Locations on Unified CM and Webex Calling
Unified CM DNs are extensions (diversion from best practice in the PA)
Local Gateway to interconnect Unified CM and Webex Calling
Flat Extension Dialling
Scenario
Calling
Site 1
Local GW
Site 3
Site 2
Internet
1501
2304
3105

## Slide 72
Alllows preservation of dialing habits in “mixed” cloud/premises sites:
Users can continue to use abbreviated dialing (e.g., 4 digits) even if the site has partially migrated to Webex Calling
When this per-location setting is enabled:
Calls made by users at this location to an unknown “extension” (i.e., same digit length as internal extensions) are routed to the selected Route Group/Trunk as “Premises” calls
Calls received by Webex Calling via trunks at this location from an unknown extension (matching extension length) are handled as “Premises” calls
Flat Extension Dialling
Recommend approach for calls to on-premises extensions

## Slide 73
Flat Extension Dialling
Unknown extension to the Premise routing
Enterprise
Trunk SJ 1
Location LA
Route Group 1
Trunk UK
Unknown Ext.
Location SJ
Unknown Ext.
Trunk LA
SJ LGW1
LA LGW
UK LGW
Location Dallas
Unknown Ext.
Location UK
Unknown Ext.
In this Location calls to unknown extensions are blocked
In these Locations calls to unknown extensions are routed to a Route Group or Trunk
Trunk SJ 2
SJ LGW2



Note: The downstream LGW and UCM must support an extension dial plan and may require a dedicated trunk for overlapping extension deployments

## Slide 74
Webex Calling user dials extension of user in other location
Webex Calling allows inter-location extension dialling
Not a problem with non-overlapping extension ranges
Flat Extension Dialling
Webex Calling to Webex Calling
Calling
Site 1
Local GW
Site 3
Site 2
Internet
1501
2304
3105
“2304”

## Slide 75
Webex Calling user dials extension of Unified CM user
Unknown extension policy is enabled for calling user’s location
Call is sent to selected destination
Unified CM dial plan routes based on extension match on DN
Flat Extension Dialling
Webex Calling to Unified CM
Calling
Site 1
Local GW
Site 3
Site 2
Internet
1501
2304
3105
“1501”

## Slide 76
Unified CM uses a flat extension dial plan
DNs are extensions
Note: not in line with best practices documented in the PA docs
Trivial setup: trunk calling search space only needs access to DN partition
Flat Extension Dialling
Webex Calling to Unified CM (UCM Dial Plan)
DN
All IP Phone DNs (extensions )
CSSs
Partitions
Trunk Inbound CSS
Webex Calling LGW
Trunk

## Slide 77
Unified CM user dials extension of Webex Calling user
Unified CM routes to Local Gateway via RP (e.g. „[23]XXX“)
Caller id is Unified CM user‘s extension
Unknown extension policy is enabled for trunk’s location  call classified as “prem”, extension dialling allowed
Call routed to Webex Calling user
Flat Extension Dialling
Unified CM to Webex Calling
Calling
Site 1
Local GW
Site 3
Site 2
Internet
1501
2304
3105
“3105”

## Slide 78
Unified CM uses a flat extension dial plan
DNs are extensions
Note: not in line with best practices documented in the PA docs
We need a route pattern to match the Webex Calling extension ranges and send them to Webex Calling
To enable callback from missed calls directory also RPs needed for
  ESN (if site prefixes are configured on Webex Calling)
  +E.164 (if caller ID format on Webex Calling is set to +E.164)
Flat Extension Dialling
Unified CM to Webex Calling (Unified CM Dial Plan)
DN
All IP Phone DNs (extensions)
CSSs
Partitions
NYCInternational
9212555.1XXX, strip Pre-Dot
NYCtoE164
[23]XXX 80112XXX 80123XXX +19295551XXX
+18105553XXX
WebexCalling
Remaining Partitions
Webex Calling RL
Webex Calling RG
Route Lists
Route Groups

## Slide 79
Unified CM uses a flat extension dial plan
DNs are extensions
Note: not in line with best practices documented in the PA docs
We need a route pattern to match the Webex Calling extension ranges and send them to Webex Calling
To enable callback from missed calls directory also RPs needed for
  ESN (if site prefixes are configured on Webex Calling)
  +E.164 (if caller ID format on Webex Calling is set to +E.164)
Flat Extension Dialling
Unified CM to Webex Calling (Unified CM Dial Plan)
DN
All IP Phone DNs (extensions)
CSSs
Partitions
NYCInternational
9212555.1XXX, strip Pre-Dot
NYCtoE164
[23]XXX 80112XXX 80123XXX +19295551XXX
+18105553XXX
WebexCalling
Remaining Partitions
Webex Calling RL
Webex Calling RG
Route Lists
Route Groups

## Slide 80
Inbound to Webex Calling, the originating trunk is identified by the otg tag inserted into the “From” header by the Local Gateway
Call classification based on location level setting for “Calls to On-Premises Extensions” > “Enable routing unknown extensions to the Premises as internal calls”
  Enabled  premises call
  Disabled and no dial plan match  external call
Before routing to the called destination, call classification determines which destinations can be reached via transit routing:
  Premises calls - allowed transit routing is WxC org number
  External calls – are rejected
Interworking between Webex Calling and Unified CM On-Premise
Unified CM via LGW to Webex Calling (Extension)
SJ Trunk A
SJ CUBE
otg=sj-lgw
Calling Party Number
1501
Premise Call
Transit Routing
WxC Org Numbers
Trunks
CCPP
Cisco PSTN
Location SJ
Unknown Ext.


## Slide 81: Interworking between Webex Calling and Dedicated Instance

## Slide 82
Connection to dedicated instance identical to integration with Unified CM
  SIP trunk between Webex Calling and DI via Local Gateway
  Dial plan configuration on both sides: DI and Webex Calling
Different for dedicated instance
  pre-provisioned Local Gateway, Webex Calling trunk, Unified CM trunk
  Cloud PSTN for DI users (route lists)
Interworking between Webex Calling and Dedicated Instance
Concepts
Calling
+12125552XXX
81212XXX
…
+14085551XXX
81401XXX
…

## Slide 83
Trunk and route group on Webex Calling multi-tenant
Location for that trunk (customer needs to set main number)
Local Gateway instance automatically provisioned (cloud managed)
SIP trunk on dedicated instance
Call routing (dial plans) still needed …
  Dedicated instance
  Webex Calling
Interworking between Webex Calling and Dedicated Instance
Pre-Configured
Calling
Pre-provisioned

## Slide 84
Interworking w/ on-premises Unified CM required during transition period
Connect Unified CM to dedicated instance or multi-tenant?
Considerations
  Dedicated instance not meant to act as tandem (session manager)
  Where does the majority of the users live?
  Capabilities: SIP/SIMPLE presence, CCNR/CCBS, …
  PSTN: (ab)use CCPP for prem users using DI as transit? Use prem PSTN for both, Webex Calling and Di?
Multi-tenant can route between users on dedicated instance and on-premises Unified CM using Webex Calling dial plans
Interworking between Webex Calling and Dedicated Instance
Interworking: Unified CM On-Premises, Webex Calling and Dedicated Instance
Calling

## Slide 85
DI and Unified CM are both “spokes” in this topology
“Default” routing to Webex Calling still not an option:
  PSTN on spokes.
  Spokes need deterministic routes to Webex Calling (and transit)
Design option: ILS/GDPR between Unified CM and DI combined with imported catalog for all Webex Calling destinations.
  Three route strings: DI, Unified CM, Webex Calling
  SIP route patterns on Unified CM and DI pointing to Webex Calling
  Webex Calling still needs a dial plan for the Unified CM destinations; routing to DI via route list
  Imported catalogs and dial plans both can be provisioned using CSVs (different format, but can be created from same data source)
GDPR mainly simplifies configuration of DI and UCM (transit routes learned automatically, same imported catalog for Webex Calling destinations on DI and Unified CM)
Interworking between Webex Calling and Dedicated Instance
Transit Routing from Unified CM to DI
Calling
PSTN
ILS/GDPR
+12125552XXX
81212XXX
…
+14085551XXX
81401XXX
…

## Slide 86
SIP route pattern for catalog’s route string needs to be provisioned in the WebexCalling partition
BAT File format (example):
  PatternType,PSTNFailover,Pattern
  pattern,2:+0,+1408555012X@example.com
  pattern,2:+0,+1212555013X@example.com
  pattern,0:+0,811011XX@example.com
GDPR PSTN failover needs to be suppressed (illegal numbers) if PSTN access for Webex Calling destinations is via UCM; else: loops!
Interworking between Webex Calling and Dedicated Instance
GDPR Imported Catalog - Example
+E.164 destination in Webex Calling
Abbreviated inter-site dialing to Webex Calling
Forcing illegal number for GDPR PSTN failover (strip/prefix). Make sure that dial plan blocks \+0! or use prefix not covered by PSTN route patterns*
*If Webex Calling is not using premises PSTN then GDPR PSTN failover actually is an alternative to using the Local Gateway trunk)

## Slide 87
Allows to share Webex Calling destinations between clusters: for example for SME deployments with centralized LGW
Calls coming into UCM from Webex Calling need access to destinations learned from other clusters via ILS/GDPR (access to remote on-net sites)
Imported +E.164 and ESN patterns end up in the same partition as destinations learned from other clusters (for example OnNetRemote)
Breaking the loop: SIP route pattern for catalog’s route string is in partition the trunk from Webex Calling does not have access to
Interworking between Webex Calling and Dedicated Instance
GDPR Imported Catalog Considerations

## Slide 88: Cloud Connected PSTN for Dedicated Instance

## Slide 89
Without route lists: „Premises“ users calling into Webex Calling via a trunk
  Call is treated as premises call based on caller ID match on dial plan pattern
  Only allowed: trunk-to-trunk and trunk-to-hosted (destination on Webex Calling)
  Not allowed/blocked: trunk-to-PSTN
Purpose of route list
  Define set of users (identified by +E.164 TN) allowed for PSTN access
  CCPP to DI: allow calls from PSTN to DI user via route group (trunk)
  DI to CCPP: allow calls from route group (trunk) to PSTN
Cloud Connected PSTN for Dedicated Instance
Why Route Lists

## Slide 90
Route Lists in Webex Calling are lists of numbers reachable through a Route Group.
Each Route List is exclusively assigned to a Location that supplies up to 40,000 unassigned numbers from the hosted pool.
Cloud Connected PSTN for Dedicated Instance
Webex Calling call routing overview
Route List
Adding PSTN numbers to Route List*
* manual, CSV, API … which is exposed to all customers (not only DI customers)

## Slide 91
Cloud Connected PSTN for Dedicated Instance
Route lists and other call routing elements
Location SJ
DI SJ Route List
+14085551001
DI Trunk 1
DI Trunk 2
Route list with
+E.164’s for DI in SJ Location
This is how Webex Calling and PSTN users reach the +E.164 numbers (users) configured on DI
Location DFW
Location DI
DI Trunk 2
This is where the
trunks “live” (dial plan context for inbound calls)
PSTN connection
CCPP 1
DI Route Group
+14085551003
…
PSTN connection
DI Trunk 1
DI DFW Route List
+19725558001
+19725558003
…
Route list with
+E.164’s for DI in DFW Location
This is how users at this location reach the PSTN
Dedicated Instance

## Slide 92
Cloud Connected PSTN for Dedicated Instance
Screening and Routing
To
 | WxC User | Trunk (RL match) | Trunk (DP match) | Cloud PSTN (CCPP or Cisco)
WxC User |  |  |  | 
Trunk (RL match on CLID) |  |  |  | 
Trunk (prem user call)* |  |  |  | 
Trunk (prem PSTN call)* |  |  |  | 
Cloud PSTN (CCPP or Cisco) |  |  |  | 
From
To
  On-premises users behind trunks cannot use Cloud PSTN, DI users can
*prem user vs PSTN: caller ID match on DP pattern, or extension
Reminder

## Slide 93
Incoming call from PSTN
Webex Calling routing lookup
Destination found in route list
Call forwarded to route list’s routing choice: route group (trunk) to DI
DI routes call to DI user
Cloud Connected PSTN for Dedicated Instance
Call Flow: PSTN to DI user
Calling
CCPP
+14085550123
+14085550124
+14085550135
…
Route List
+14085550124
+14085550123
+14085550124
+14085550135
…
Route List
+14085550124

## Slide 94
Unified CM route lookup
Send to PSTN (SIP trunk to Webex Calling)
Webex Calling lookup to classify call
Caller id found in route list  cloud PSTN access allowed
Webex Calling route lookup
  Routing context: trunk’s location
Call sent to trunk location’s PSTN choice
Cloud Connected PSTN for Dedicated Instance
Call Flow: DI user to PSTN user
Calling
CCPP
+14085550123
+14085550124
+14085550135
…
Route List
+14085550123
+14085550124
+14085550135
…
Route List
+14085550124

## Slide 95: Q&A

## Slide 97: Additional Slides

## Slide 98
What if extension ranges of sites overlap?
  No extension dialing between sites
  Alice can call Bob and Charlie using extension dialing
  Alice cannot call Dave using extension dialing
  What if Charlie dials 4002?
Webex Calling Multi-Tenant Dial Plan Foundations
Understanding location codes
NY
+12125556001
Charlie
Widgets, Inc.
Montreal
4002
Dave
LA
4002
+13105554002
Bob
4001
+13105554001
Alice

## Slide 99
To avoid timeouts, conflicts need to be avoided between:
  First digit of extensions
  Internal steering digit
  Outbound dial digit
Example: steering digit 8, 4D extensions, 4D location code
What if Alice lifts the handset and starts to dials 8, 2, 0, 2? Bob, Charlie?
Webex Calling Multi-Tenant Dial Plan Foundations
Conflicts
NY
6001
82026001
+12125556001
Charlie
Widgets, Inc.
Montreal
4001
82514001
+15145554001
Dave
LA
8202
82018202
+13105558202
Bob
8001
82018001
+13105558001
Alice
Location | Location Code
LA | 8201
NY | 8202
Montreal | 8251

## Slide 100
Load balancing and failover across trunks to premises (scale, redundancy)
Communication between Cloud Connected PSTN users and premises users
Ability to route calls to different premises PBX’s based on:
  E.164’s/DID’s
  ESN’s (e.g., 8+site code+extension)
  SIP URI’s (Webex Calling to PBX only)
“Tandem” functionality to route calls between premises PBX’s
Broader range of migration and co-existence scenarios with premises PBX’s, including “mixed” sites with premises users and Webex Calling users
Better visibility of call routing decisions
Webex Calling Multi-Tenant Dial Plan Foundations
Benefits of trunks, route groups and dial plans

## Slide 101
Represents a single SIP Trunk to an on-premises device (currently, only CUBE is supported)
Must be assigned to a Location
Can be included in one or more Route Groups
Webex Calling Multi-Tenant Dial Plan Foundations
Trunks connecting to on-premises devices
Internet
Dallas
Local Gateway
Webex endpoints
On-prem PBX
DFW Trunk A
PSTN

## Slide 102
Logical grouping of Trunks (max. 10) for scale and redundancy of connections to the premises
Does not “live” in a Location
Webex Calling Multi-Tenant Dial Plan Foundations
Route groups - Scale and redundancy for trunks
US East (Route Group)
NY Trunk A
NY Trunk B
ny-LGW-A
ny-LGW-B
1
1
2
Random pick
DFW Trunk A
dfw-LGW-A
DFW Trunk B
dfw-LGW-B
2
Random
pick
Calls distributed randomly among Trunks with same priority
If a Trunk with lower priority order (1) is not available, system attempts to route call to a Trunk with a higher priority order (2)

## Slide 103
Same trunks can be member of different Route Groups
Example:
Same set of trunks used by different Route Groups and have different prioity in each Route Group
Route Group NY prefers NY trunks and uses DFW as backup/overflow
Route Group DFW pefers DFW trunks ans uses NY as backup/overflow
Webex Calling Multi-Tenant Dial Plan Foundations
Route groups - Trunks in multiple route groups
NY Trunk A
NY Trunk B
ny-LGW-A
ny-LGW-B
DFW Trunk A
dfw-LGW-A
DFW Trunk B
dfw-LGW-B
NY (Route Group)
DFW (Route Group)

## Slide 104
Start with group of trunks that have lowest priority value
Randomly pick one trunk from that group and try that trunk
On failure randomly pick a different trunk with same priority
SIP causes 401, 407, 480, 606 (if there has been no prior 18x response)
All other 4xx except 403, 404, 410, 413, 484, 486
All 5xx
SIP timeout (12 seconds)
If all trunks with this priority failed advance to next priority and repeat
Webex Calling Multi-Tenant Dial Plan Foundations
Trunk selection, route advance

## Slide 105
Dial plans allow you to route calls to on-premises destinations by use of trunks or route groups. They are configured globally for an enterprise and apply to all users, regardless of location.
A dial plan also specifies the routing choice (trunk or route group) for calls that match any of its dial patterns. Specific dial patterns can be defined as part of your dial plan.
A dial pattern represents on-premises extensions:
  ESN/on-net numbers
  +E.164 patterns
  SIP URI domains
Webex Calling Multi-Tenant Dial Plan Foundations
Dial Plans

## Slide 106
Only domains (right-hand side of SIP URI after @) are matched
Either:
Fully qualified domain
Domain with a leading “*.” indicating all sub-domains of given domain
Examples:
Webex Calling Multi-Tenant Dial Plan Foundations
Dial Plan - SIP URI dial pattern syntax
Prefix | Meaning | Examples
example.com | only URIs with host portion “example.com” | alice@example.com
us.example.com | only URIs with host portion “us.example.com” | alice@us.example.com
*.example.com | URIs with host portion being sub-domain of “example.com” | alice@eu.example.com alice@sales.us.example.com Note: alice@example.com is not matched!

## Slide 107
Webex Calling Multi-Tenant Dial Plan Foundations
Dial Plans
Enterprise
SJ Trunk A
CA-RG-1 Route Group
UK Trunk A
Location SJ
LA Trunk A
SJ CUBE
LA CUBE
UK CUBE
#1
#2
Location UK
CA PBX Dial Plan
us.foo.com
8408XXXX
+1408525XXXX
Trunk SJ
UK PBX Dial Plan
uk.foo.com
8442XXXX
+442022!
Trunk UK
8310XXXX
+1310444XXXX
Location LA
Trunk LA
Dial Plans are defined globally for an Enterprise and apply to all their users regardless of Location
   Routing choice for given Dial Pattern is same for everybody

## Slide 108
Load balancing and failover across trunks to premises (scale, redundancy)
Webex Calling Multi-Tenant Dial Plan Foundations
Load balancing and failover
Site 3
Local GW
Cisco Calling Plan
PSTN
CCPP
Internet
Local Gateway Trunk

## Slide 109
Load balancing and failover across trunks to premises (scale, redundancy)
Communication between Cloud Connected PSTN users and premises users
Webex Calling Multitenant Dial Plan Foundations
Combine Cloud PSTN with premises trunks
Internet
Local GW
Site 3
Local Gateway Trunk
+12125552XXX
81212XXX
…
Cisco Calling Plan
PSTN
CCPP

## Slide 110
Ability to route calls to different premises PBX’s
Webex Calling Multi-Tenant Dial Plan Foundations
On-premises PBX routing
Internet
PSTN
Site 3
Local GW
Local Gateway Trunk
Local GW
Local Gateway Trunk
+14085551XXX
81401XXX
…
+12125552XXX
81212XXX
…
Cisco Calling Plan
CCPP

## Slide 111
Ability to route calls to different premises PBX’s
“Tandem” functionality to route calls between premises PBX’s
Webex Calling Multi-Tenant Dial Plan Foundations
On-premises PBX routing
Internet
PSTN
Site 3
Local GW
Local Gateway Trunk
Local GW
Local Gateway Trunk
+14085551XXX
81401XXX
…
+12125552XXX
81212XXX
…
Cisco Calling Plan
CCPP

## Slide 112
Some users are on Webex Calling and others in the same location are on Unified CM
Users want to be able to use abbreviated intra-site dialling within a site (across call controls)
Example: Bob want to be able to Dial 4002 to reach Alice
Webex Calling Multi-Tenant Dial Plan Foundations
Mixed/split sites
Dallas
Dallas LGW
NY
Bob 4001
Alice 4002
Internet
PSTN
Cisco Calling Plan
CCPP

## Slide 113
Some users are on Webex Calling and others in the same location are on Unified CM
Users want to be able to use abbreviated intra-site dialling within a site (across call controls)
Example: Bob want to be able to Dial 4002 to reach Alice
Webex Calling Multi-Tenant Dial Plan Foundations
Mixed/split sites
Dallas
Dallas LGW
NY
Bob 4001
Alice 4002
Internet
PSTN
Cisco Calling Plan
CCPP

## Slide 114
Some users are on Webex Calling and others in the same location are on Unified CM
Users want to be able to use abbreviated intra-site dialling within a site (across call controls)
Example: Bob want to be able to Dial 4002 to reach Alice
Webex Calling Multi-Tenant Dial Plan Foundations
Mixed/split sites
Dallas
Dallas LGW
NY
Bob 4001
Alice 4002
Internet
PSTN
Cisco Calling Plan
CCPP
“4002” is not a Webex Calling number and no match in dial plan .. but it “looks” like an an extension (2-6 digits)  route it!
Signaling path only; media path with ICE is different

## Slide 115
Call classified as “premises” inbound into Webex Calling based on caller id match on DP pattern
Sent to trunk/RG based on DP match
Webex Calling Multi-Tenant Dial Plan Foundations
Call between PBX users
Site 1
PSTN
Local GW
Internet
Site 3
Enterprise A
Site 1
Local GW
Cisco Calling Plan
CCPP

## Slide 116
Sent to user based on match on DID, extension or ESN
Webex Calling Multi-Tenant Dial Plan Foundations
PBX user or PSTN to Webex Calling user
PSTN
Internet
Site 1
Local GW
Site 3
Enterprise A
Site 1
Local GW
Cisco Calling Plan
CCPP

## Slide 117
PBX user dials a PSTN destination
PBX sends call to Webex Calling via trunk
Call is blocked (no transit)
PBX should never route PSTN calls to Webex Calling
Webex Calling Multi-Tenant Dial Plan Foundations
PBX user or PSTN to Webex Calling user
Internet
Site 1
Local GW
Site 3
Enterprise A
Site 1
Local GW
Cisco Calling Plan
CCPP
PSTN

## Slide 118
Depending on the number of Webex Calling TN ranges maintaining the set of Webex Calling RPs can be complex
Alternative: use GDPR imported catalog with set of Webex Calling TN ranges
SIP route pattern for catalog’s route string needs to be provisioned in the WebexCalling partition
BAT File format (example):
  PatternType,PSTNFailover,Pattern
  pattern,2:+0,+1408555012X@example.com
  pattern,2:+0,+1212555013X@example.com
  pattern,0:+0,811011XX@example.com
GDPR PSTN failover needs to be suppressed (illegal numbers) if PSTN access for Webex Calling destinations is via UCM; else: loops!
Routing between Webex Calling and Unified CM (including DI)
Dial Plan Maintenance

## Slide 119
Depending on the number of Webex Calling TN ranges maintaining the set of Webex Calling RPs can be complex
Alternative: use GDPR imported catalog with set of Webex Calling TN ranges
SIP route pattern for catalog’s route string needs to be provisioned in the WebexCalling partition
BAT File format (example):
  PatternType,PSTNFailover,Pattern
  pattern,2:+0,+1408555012X@example.com
  pattern,2:+0,+1212555013X@example.com
  pattern,0:+0,811011XX@example.com
GDPR PSTN failover needs to be suppressed (illegal numbers) if PSTN access for Webex Calling destinations is via UCM; else: loops!
Routing between Webex Calling and Unified CM (including DI)
Dial Plan Maintenance
+E.164 destination in Webex Calling
Abbreviated inter-site dialing to Webex Calling
Forcing illegal number for GDPR PSTN failover (strip/prefix). Make sure that dial plan blocks \+0! or use prefix not covered by PSTN route patterns*
*If Webex Calling users use cloud PSTN then GDPR PSTN failover actually is an option. In that case use “0:” as strip/prefix instruction for +E.164 destinations

## Slide 120
Allows to share Webex Calling destinations between clusters: for example for SME deployments with centralized LGW
Calls coming into UCM from Webex Calling need access to non-Webex Calling destinations learned from ILS/GDPR (access to remote on-net sites)
Imported +E.164 and ESN patterns end up in the same partition (for example OnNetRemote)
Breaking the loop: SIP route pattern for imported catalog’s route string is in partition the trunk from Webex Calling does not have access to
Routing between Webex Calling and Unified CM (including DI)
GDPR Imported Catalog Considerations

## Slide 121
Proper dial plan design (see Enterprise PA* for details) enables seamless transition of DNs from UCM to Webex Calling
  All dialing habits are possible: ESN, DN and +E.164
Detailed information in the “Cisco Preferred Architecture for Webex Calling”: https://www.cisco.com/c/dam/en/us/td/docs/solutions/CVD/Collaboration/hybrid/AltDesigns/PA-WbxCall.pdf
Routing between Webex Calling and Unified CM (including DI)
GDPR Imported Catalog Considerations
*Preferred Architecture for Cisco Collaboration 14 Enterprise On-Premises Deployments, CVD *https://www.cisco.com/c/en/us/td/docs/solutions/CVD/Collaboration/enterprise/14/collbcvd.html

## Slide 122
Local Gateway concurrent session limitations
Integration between Webex Calling and UCM (or dedicated instance) is pure call routing integration*
No concept of sharing call state nor user (line) presence
Impact on any feature relying on call state or presence:
Call pick-up (notifications)
Hunt: no way to determine state of line
..
Also: no cross call control hoteling (extension mobility)
Keep users of these features together on a single call control instance
Interworking to Cloud Calling
Interworking Limitations

## Slide 123
Cloud Connected PSTN (CCP) for Dedicated Instance
Route Lists - Multiple DI clusters
Location SJ
DI 1 SJ Route List
+14085551001
DI 1 Trunk 1
DI 1 Trunk 2
Route list with
+E.164’s for DI 1 in SJ Location
This is how Webex Calling and PSTN users reach these +E.164 numbers used by DI 1 in SJ
Location DI 2
DI 2 Trunk 2
This is where the
trunks to the DI’s “live” (dial plan context for inbound calls)
PSTN connection
CCP 1
DI 1 Route Group
+14085551003
…
DI 2 Trunk 1
DI 2 DFW Route List
+14087778001
+14087778003
…
Route list with
+E.164’s for DI 2 in SJ Location
This is how Dedicated Instance and Webex Calling users at this location reach the PSTN
Location DI 1
DI 1 Trunk 2
DI 1 Trunk 1
DI 2 Trunk 1
DI 2 Trunk 2
DI 2 Route Group
This is how Webex Calling and PSTN users reach these +E.164 numbers used by DI 2 in SJ
Dedicated Instance 1
Dedicated Instance 2